## Slide 1: 3-Level NPC Inverters
Thesis: DC-LINK CAPACITOR SIZING OF THREE-LEVEL NEUTRAL POINT
CLAMPED VOLTAGE SOURCE INVERTERS FOR VARIABLE SPEED DRIVES

## Slide 2: Advantages & Disadvantages
Advantages against 2-Level Inverter:
- Efficiency
- 1/2Vdc voltage stress
Disadvantages against 2-Level Inverter :
- Complexity
- Unequal Power Loss

## Slide 3: Sinusoidal PWM
Phase voltages (reference signals);
Two triangular carrier signal
[0,Vdc/2] & [-Vdc/2,0]
Peak amplitude=Vdc/2

## Slide 4: Sinusoidal PWM
State | Q1 | Q2 | Q3 | Q4
Carrier1<reference Carrier2<reference | ON | ON | OFF | OFF
Carrier1>reference Carrier2<reference | OFF | ON | ON | OFF
Carrier1<reference Carrier2>reference | OFF | ON | ON | OFF
Carrier1>reference Carrier2>reference | OFF | OFF | ON | ON

## Slide 5: Sinusoidal PWM
This method does not control the neutral point.
Large capacitors needed.
Worse case for low frequency NPP ripple can be expected at
high modulation index
high load current
low fundamental frequency
low power factor for SPWM modulation.

## Slide 6: SVPWM
Applicable but more complex.
Switching States:
State | Q1 | Q2 | Q3 | Q4
P (S1) | ON | ON | OFF | OFF
O (S2) | OFF | ON | ON | OFF
N (S3) | OFF | OFF | ON | ON

## Slide 7: SVPWM
State S1(P): Output voltage: Vdc/2. (voltage difference between node and neutral point)
State S2(O): Middle switches are ON. Output voltage is 0.
State S3(N): Bottom 2 switches are ON. Output voltage: -Vdc/2

## Slide 8: SVPWM
Totally 27 switching states
All possible switching states represented at the left.
Vectors have different lengths.
Largest vectors are obtained when all phases have non-O states.
Middle vectors: one phase at O-state.
Small vectors: two phases at O-state. Two alternative vectors for small vectors.

## Slide 9: SVPWM
required output vector is obtained by using four vectors.
Six major regions. Each major regions have six sub regions.
Va | Vb | Vc | Main Sector | Center vector
>0 | <0 | <0 | 1 | PNN
>0 | >0 | <0 | 2 | PPN
<0 | >0 | <0 | 3 | NPN
<0 | >0 | >0 | 4 | NPP
<0 | <0 | >0 | 5 | NNP
>0 | <0 | >0 | 6 | PNP

## Slide 10: SVPWM
Subregions of Major Region 1
Each subregion has at least four vectors.
Space vector hexagon of two-level inverter and subregions of major region are similar

## Slide 11: SVPWM
Move vector at the center of hexagon.

## Slide 12: SVPWM
Vector sequences:
Time sequence
Vector sequence

## Slide 13: NPP Control
2 types NPP ripple:
Fundamental freq.
Switching freq.